## Slide 1: Memory Interfacing in 8085

## Slide 2
Interfacing is nothing but connecting outside peripherals to 8085 Microprocessor.
Interface is a path of communication between two components.
Interfacing is a technique of connecting microprocessor with memory.
When microprocessor is executing an instruction, it needs to access the memory for reading instruction codes and the data.
For interfacing, both the memory and the microprocessor require some signals to read from and write to registers.
Interfacing process needs to match the memory requirements and microprocessor signals.

## Slide 3
8085 Microprocessor – 16 Address Lines (A0 – A15)
2^16 = 65536 bits = 64 KB memory.
Addresses start from 0000H to FFFFH – Addresses of the memory locations which can be addressed by the 8085 microprocessor.
8085 microprocessor uses the three control signals for the interfacing –
  IO/M’ – Input/Output or Memory
  RD’ – Read
  WR’ – Write

## Slide 4
In response to these three signals the memory chips have also some signals –
  CE’ or CS’ – Chip enable or Chip select signal
  OE’ or RD’ – Output Enable or Read Signal (Read Operation)
  WE’ or WR’ – Write Enable or Write Signal (Write Operation)
  IO/M’ RD’ WR’
  0 0 1 - 8085 reads data from memory
  0 1 0 - 8085 writes data into the memory
  These three signals are combined to generate two signals MEMR’ and MEMW’.

## Slide 5
IO/M’ + RD’ = MEMR’ (0+0=0)
IO/M’ + WR’ = MEMW’ (0+0=0)
If IO/M’=1 then MEMR’ and MEMW’ signals will be deactivated irrespective of the value of RD’ and WR’ signals.

## Slide 6
Representation of memory chip is mxn
Where, m = number of memory location/memory size
n = number of bits in each memory location
e.g. 256X8 (256 B) memory.
m = 256 = 2^8, so there are 8 address lines
n = 8, there are 8 data lines.
Prob.: Find the length of address and data bus of 2048X512 memory chip.
Sol.: 2048X512 = (2^11)X512
So, length of address = 11 and number of data lines = 512 (Answer)

## Slide 7
Number of memory ICs required to construct a memory.
Number of ICs required = Memory to be designed / Available capacity.
Prob.: Construct 32 KB memory using 256X4 ICs.
Sol.: Number of 256X4 ICs = [32X(2^10)X8]/[256X4]
= [32X(2^10)X8]/[(2^8)X4] = 32X2^2X2 = 32X4X2 = 256
Altogether there will be 128 rows and in each row there are two 256X4 ICs
Because in 32KB, there are 8 data line whereas in 256X4, there are 4 data lines.
Prob.: Find number of 256X8 ROM chip required to design 8KB of memory.
Sol.: 256X8 = 256 B and 256X4 = 1024 B = 1 KB
To design 1 KB requires 4 chips
so, to design 8 KB requires = 8X4 = 32 Chips.
Number of Chips = 8 KB / (256X8) = [8X(2^10)X8]/[(2^8)X8] = 8X2^2 = 8X4 = 32

## Slide 8
Peripherals are connected to microprocessor by two modes –
  Memory mapped I/O mode (I/O devices are treated as memory ICs) and I/O mapped I/O mode
 | Memory mapped I/O |  | I/O mapped I/O | 
Number of Address lines | 16 | 16 | 16 | 8
Control Signals | MEMR’ MEMW’ | MEMR’ MEMW’ | MEMR’ MEMW’ | IOR’ IOW’
Number of peripherals | 64 KB Mem.+I/O (e.g. 64+0, 50+14) |  | 64 KB | 2^8 = 256 I/O devices

## Slide 9
Memory mapped I/O:
Advantages:
  IO/M’ is not required. So no separate instructions are needed.
  Arithmetic, logical operations can be directly performed on I/O data.
Disadvantages:
  Interfacing is complex.
  Memory space required is high.

## Slide 10
I/O mapped I/O:
Advantages:
  Interfacing is less complex.
  Maximum capacity of microprocessor will be utilized.
Disadvantages:
  I/O devices require separate instructions.
  Arithmetic, logical operations can’t be performed on I/O data.
  4 control signals required.