## Slide 1
Microcomputer and System Bus

## Slide 2: Block Diagram of a Simple Microcomputer:

## Slide 3: Microcomputer Structure
INPUT
OUTPUT
I/O PORTS
CPU
MEMORY( RAM AND ROM)
DATA BUS
CONTROL BUS
CONTROL BUS
ADDRESS BUS

## Slide 4: Block Diagram of a Simple Microcomputer:
Components of Microcomputer:
  CPU
  Memory
  Input / Output circuitry
  System Buses:
      Address bus
      Data bus
      Control bus

## Slide 5: Microcomputer Structure
A Microcomputer system is one which uses a microprocessor as its CPU.
In addition the Microcomputer also has a memory unit, input/output devices and system buses.
It consists - Address Bus, Data Bus, Control Bus
What is a Bus?
A group of lines used to transfer bits between microprocessor and other system components like memory and I/O devices.

## Slide 6: CPU - Central Processing Unit
It controls the operation of computer
The CPU fetches binary-coded instructions from memory
Decodes the instructions into a series of simple actions
Carries out these actions in a sequence of steps
Important components: IP (Instruction Pointer), General purpose registers and Control bus signal generating circuits

## Slide 7: CPU
Fetches the binary-coded instructions from memory, decodes the instructions into a series of actions and carries out these actions in a sequence of steps.
Contains an address register to hold the address of next instruction to be fetched from memory.
General purpose registers to store binary data temporarily, and circuitry to generate the control bus signal.

## Slide 8: Memory
It usually consists of a mixture of RAM and ROM. It may also have hard disks or optical disks.
Two purposes:
  Store the binary codes of instructions
  Store the binary coded data

## Slide 9: Memory:
It stores the binary codes for the sequence of instructions and binary coded data. Example: ROM, RAM and Magnetic disks
RAM can be read and written to anytime the CPU commands it, but ROM is pre-loaded with data and software that never changes, so the CPU can only read from it.
ROM is typically used to store the computer's initial start-up instructions.
In general, the contents of RAM are erased when the power to the computer is turned off, but ROM retains its data indefinitely.
In a PC, the ROM contains a specialized program called the BIOS that orchestrates loading the computer's operating system from the hard disk drive into RAM whenever the computer is turned on or reset.

## Slide 10: System Bus:
The microcomputer’s system bus contains three buses: address, data, and control bus
When a memory or an I/O chip receives data from the microprocessor, it is called a WRITE operation, and data is written into a selected memory location or an I/O port (register).
When a memory or an I/O chip sends data to the microprocessor, it is called a READ operation, and data is read from a selected memory location or an I/O port.

## Slide 11: Address bus
Consists of 16, 20, 24, 32, or 36 parallel signal lines. Therefore it is that bit long.
The number of locations that the CPU can address is determined by the number of address lines.
On these lines the CPU sends out the address of the memory location.
If the CPU has N address lines then it can directly address 2N memory locations.

## Slide 12: Address Bus:
It is a Unidirectional bus.
Information transfer takes place from the MP to the memory or I/O elements.
On these lines the CPU sends out the address of the memory location or I/O port that is to be written to or read from.
For example : microprocessor with 32 address pins can generate
232= 4,294,964,296 bytes
Example : if address line 16 then 216 memory locations

## Slide 13: Control Bus:
It consists of a number of signals that are used to synchronize operation of the individual microcomputer elements.
Consists of potentially many signals. Typically:-
    Read
    Write
    Interrupt control
    Bus control signals for DMA (Direct Memory Access)

## Slide 14: Control bus
4 to 10 parallel signal lines
CPU sends signal on the control bus to enable the outputs of addressed memory devices.
Memory Read, Memory Write, I/O Read, I/O Write.
To read a byte of data the CPU sends out the memory address of the desired byte on the address bus and sends out Memory Read signal.

## Slide 15: Data Bus:
It is a bidirectional bus, i.e. CPU can read or send data both
Data can flow in both directions, that is, to or from the microprocessor.
The size of the data bus varies from one microprocessor to another.
Usually matches the word length of the microprocessor
Usually a multiple of 8
We talk of 4-bit (nibble), 8-bit, 16-bit , 32-bit and 64-bit processors which refers to the normal word length of the microprocessor.

## Slide 16: Input/Output
Allows the computer to take in data from the outside world or send data to the outside world.
Keyboards, monitor, printer are connected to I/O section.

## Slide 17: I/O Unit:
Input/output (I/O), refers to the communication between an information processing system (such as a computer), and the outside world possibly a human, or another information processing system.
Inputs are the signals or data received by the system, and outputs are the signals or data sent from it.
Devices that provide input or output to the computer are called peripherals like the keyboard and mouse, and output devices such as the display and printer, hard disk drives and optical disc drives serve as both input and output devices.
Computer networking is another form of I/O.

## Slide 18: Fetching & Execution Cycles:
Fetching Cycles
  The fetch cycle takes the instruction required from memory, stores it in the instruction register, and
  Moves the program counter by one so that it points to the next instruction.
Execute cycle
  The actual actions which occur during the execute cycle of an instruction.
  Depends on both the instruction itself and the addressing mode specified to be used to access the data that may be required.

## Slide 19: Fetching & Execution Cycles:
Step 1
  Instruction Pointer (IP) or a program counter is a register, that holds the address of the next instruction to be fetched.

## Slide 20: Fetching & Execution Cycles:
Step 2

## Slide 21: Fetching & Execution Cycles:
Step 3

## Slide 22: Fetching & Execution Cycles:
Step 4

## Slide 23: Fetching & Execution Cycles:
Step 5

## Slide 24: Fetching & Execution Cycles:
Step 6

## Slide 25: Simple Microcomputer - All Bus Operation
A microcomputer fetches each program instruction in sequence, decodes the instruction and executes it.
The CPU in a microcomputer reads data from memory by sending out an address on the address bus and a Memory Read signal on the control bus. The memory output the addressed instruction or data word to the CPU on the data bus.
The CPU writes a data word to memory by sending out an address on the address bus, sending out the data word on the data bus and sends a Memory Write signal to memory on the control bus.
To read data from a port the CPU sends out the port address on the address bus and send an I/O Read signal to the port device on the control bus. Data from the port comes into the CPU on the data bus.
To write data to a port the CPU sends out the port address on the address bus, sends out the data to be written to the port on the data bus, and sends an I/O Write signal to the port device on the control bus.