## Slide 1: Some Important Pins of 8085 Microprocessor

## Slide 2
Some important Pins of 8085 Microprocessor
ALE, IO/M’, RD’, WR’, S1, S0.
ALE (Address Latch Enable): ALE is a control pin which controls if ALE = 1 then the multiplexed lines of address and data will carry only address. So, AD0 – AD7 = A0 – A7. When ALE = 0 then the multiplexed lines of address and data will carry only data. So, AD0 – AD7 = D0 – D7. So based on ALE the multiplexed lines are going to carry the address or data.
IO/M’: If IO/M’ = 1 then it’s a I/O operation and If IO/M’ = 0 then it’s a memory operation.
RD’, WR’: Both are active low pin. If RD’ = 0 then it’s a Read operation and WR’ = 0 then it’s a write operation. But at the same time RD’ and WR’ can’t be zero.

## Slide 3
S1, S0 : With the combination of status lines we can define the machine cycle. When S0 and S1 are 1 and 0 then it will be Read operation and when S0 and S1 are 0 and 1 then it will be Write operation.
IO/M’ S1 S0
0 0 1 Memory Read
0 1 0 Memory Write
0 1 1 Opcode Fetch
1 0 1 I/O Read
1 1 0 I/O Write
1 1 1 Interrupt Acknowledgement

## Slide 4
  8085 is a 40-pin IC, works on +5V supply.
  It has 8 data lines and 16 address lines.
  Lower order address data bus (AD0 – AD7) is multiplexed and ALE signal is used for de-multiplexing.
  It has five hardware interrupts.
  It support DMA data transfer using HOLD and HLDA signals.
  Slower peripheral can be connected to this processor with the help of READY signal.
  It support serial devices with SID and SOD pins.